## Slide 1
Infrastructure For Real-Time Video Call Service

## Slide 2: Tango – Communications, Social, Content

## Slide 3: What is SWIFT?
SWIFT stands for -
“Secured Wireless session Initiate Framework for Tango”
Innovated and patented protocol by Tango
Supports Tango’s infrastructure of real-time video call service

## Slide 4: Outline
Why was SWIFT developed?
Overview of SWIFT Protocol
Authentication
Firewall Traversal
Geographic Load Balancing
Stateless Server Design
Network Switch without Call Drop
Smart Relay Routing

## Slide 5: What is protocol to establish a call over Internet
Parties
  Caller: initiate a call
  Callee: receive a call
  Server: help set up real-time channel
Goal
  Quickly set up the best high-quality channel between caller and callee to transmit voice and video

## Slide 6: Traditional Protocol Jingle/SIP + TURN Overview
Jingle/SIP + TURN
  Jingle/SIP: signaling protocol to exchange metadata including peer-to-peer candidates (internal/external/relay addresses) between caller and callee
  TURN (Traversal Using Relays around NAT): used for NAT traversal (peer-to-peer, i.e., P2P) and relay
Protocol Deficient
  Too many round trips to establish a call, particularly bad over wireless networks

## Slide 7: Jingle+TURN solution Tango used before SWIFT
XMPP Server
Caller
Callee
Push Service
Push
Login
Exchange meta data
UDP channel set up
(peer-to-peer or relay)
Push request

## Slide 8: Tango: Jingle+TURN before SWIFT
CalleR
XMPP Server
CalleE
TURN
Authentication
P2P Candidate
TURN
P2P Negotiation
Push Request
Presence
Initiate (P2P cands)
Accept
Push Notification
(Apple/Google/Tango)
Login (several RTTs)
Presence
Initiate
Accept (P2P cands)
P2P Candidate
P2P Negotiation
TURN
TURN
Waiting Call
Authentication
Round Trips:

## Slide 9: Issues of Jingle+TURN solution
Jingle+TURN solution
  Too many client-server round trips to establish a call
    TCP: 1.5 RTTs
    SSL: 2.5 RTTs
    Authentication (SASL): ~7 RTTs
    Other RTTs (push/P2P/jingle session msg): ~6 RTTs
  TCP has retransmission timeout exponential back-off (from 1.5 sec)
    Particularly poor on wireless network
    Difficult to control this at the application layer

## Slide 10: SWIFT protocol design target
Fast
  Less round trips (3 client-server round trips)
  Fast retransmission (UDP by default)
  All-in-one server (connecting/NAT traversal/relay)
Robust
  STATELESS server design
  Near-seamlessly Cellular/WiFi switch support
Easy to scale and geo-localize
  Servers are independent to each other

## Slide 11: SWIFT protocol (1st round trip)
Backend
SWIFT Server
Caller
Callee
Push
Request
Push Notification
(SWIFT public address)
Push Request
Opportunistic
SWIFT Push
Callee Information & Call Configuration
Push Response
Push Notification Service
Apple
Google
Microsoft
Tango

## Slide 12: SWIFT protocol (2nd round trip)
Backend
SWIFT Server
Caller
Callee
Connect to Caller
Configuration Request
Configuration
Response
Configuration
Callee’s External Address
& Configuration

## Slide 13: SWIFT protocol (3rd round trip)
SWIFT Server
Caller
Callee
Connect Ack
Connect Ack (Caller’s External Address)
Connection is established in 3 round trips
A relay channel is ready to use
UDP based protocol (control retransmission ourselves)

## Slide 14: SWIFT peer-to-peer channel
SWIFT Server
Caller
Callee
SWIFT Regular NAT Traversal
If NAT traversal (P2P) succeeds, we will seamlessly switch to P2P channel
SWIFT NAT Symm Traversal
Relay channel

## Slide 15: Protocol State Machine (client only)
Handle communication between server and client
Handle retransmission on UDP
Handle NAT traversal

## Slide 16: Authentication
Based on auth token, which is inside every control packet
  No extra authentication round trips needed
  No database access needed
  Timestamp/sequence is used to prevent packet replay attack
Client
Registration server
SWIFT auth token:
Signed username
Signed password
Username/
password
SWIFT server
Server Shared Key
Server Shared Key
SWIFT auth token in packet header
Packet payload/timestamp/sequence is encrypted by password
Hash of payload in packet header
Decrypt:
Use shared key decrypt SWIFT auth token
Use password decrypt payload
Verify hash
Verify timestamp/sequence

## Slide 17: Firewall Traversal
How to connect if UDP is blocked?
  Use TCP with port 443 (SSL port)
  Client will connect to the server using UDP and TCP at the same time
    No delay in terms of firewall traversal
  TCP will be disconnected immediately after UDP goes through
Caller
Callee
SWIFT server
UDP
UDP
TCP
TCP

## Slide 18: Geographic Load balancing
Caller
Callee
In US
Each server is independent
In China
Push notification
Contains public IP:port of SWIFT server
Geo-aware DNS with round robin
By CEDEXIS
US
Servers
Ireland
Servers
Singapore
Servers
Pulled to the same server

## Slide 19: SWIFT Performance
Faster connecting
  5x~10x faster than Jingle+TURN Protocol
Higher connection success rate
Over 30% more calls connected daily than Jingle+TURN Protocol

## Slide 20: Stateless Design on Server
No session/presence states kept on server
We only keep a simple routing table
    The table can be rebuilt even if the SWIFT server restarts.
    No calls will be dropped.
Key to the service robustness
      - WiFi/Cellular switch in call
      - WiFi/Cellular initiating and receiving call
      - Some phones may disconnect WiFi when the phone is asleep
  - Smart relay routing
client username | address
usernameA | IP:port of A
usernameB | IP:port of B

## Slide 21: Handle Network Switch
Purpose - no call drop when switching network (either in call or calling)
  Enter a WiFi from the cellular network
  Moving out of a WiFi area to the cellular network
SWIFT Server
Client A
Client B
P2P channel
LTE
WiFi
Keep alive heartbeat
Keep alive heartbeat
P2P channel
Re-auth with keep-alive
Back to relay channel
Switch to new P2P channel

## Slide 22: How to find the best server to relay?
We have 30%~40% relay calls (not P2P)
Geo-aware DNS result is not working well
  Observation 1: Relay server is not equivalent between sites (US vs China)
  Observation 2: US servers are better for the Middle East clients than Ireland servers, though it is geographically further
  Observation 3: Sometimes two-hop relay is faster than a one-hop relay
SWIFT Server (US)
Client A (US)
Client B (China)
50 ms
SWIFT Server
(China)
30 ms
Long delay link
300 ms
600 ms

## Slide 23: Geo-Aware DNS issues (cont.)
Geo-aware DNS result is not working well (cont.)
  Observation 4: Latency could be quite different between a single client and different servers even in one country
  Observation 5: Delay between one client and one server could be variable over time
    Below is a network “ping” result from a China machine to 3 different US servers

## Slide 24: SWIFT Smart Routing for Relay Traffic
First location the 4 best “candidate SWIFT servers”
  A) The server DNS returns (usually close to caller)
  B) The closest server to caller (Server 1)
  C) The closest server to callee (Server 3)
  D) The closest middle server in terms of the sum of delays to caller and callee (Server 2)
Server 1
Caller
Callee
20 ms
Server 2
30 ms
120 ms
Server 3
130 ms
300 ms
350 ms

## Slide 25: How to find the best server to relay?
Search the best path among all possible 1-hop and 2-hop paths through the 4 candidate servers
  Probing packets are sent every 30 seconds end-to-end through different paths
  The path would be seamlessly switched if a better one is found
Server (caller)
Caller
Callee
Server (middle)
Server (callee)
Server (DNS)

## Slide 26: RTT improvement (A/B test)
Chart: Audio only RTT Smart Routing (Enabled/Disabled)
| IL | KW | TR | SA | CN | KR | UK | DE | MY | ALLOTHER | HK | ALL | ALLTOP | TW | TH | MX | IT | ES | US
RTT | 0.70655 | 0.73504 | 0.75161 | 0.76222 | 0.77354 | 0.78697 | 0.81673 | 0.83293 | 0.85589 | 0.89809 | 0.90975 | 0.9138 | 0.92428 | 0.94372 | 0.96482 | 1.0004 | 1.002 | 1.0027 | 1.006
kbps

## Slide 27: Bitrate Improvement (A/B test)
Chart: Video Bitrate Smart Routing (Enable/Disable)
| IL | KW | SA | CN | TR | ES | ALLOTHER | MY | KR | TH | ALL | ALLTOP | DE | UK | HK | US | TW | MX | IT
Biterate Improvement | 1.7857 | 1.5723 | 1.5262 | 1.3928 | 1.3831 | 1.181 | 1.1738 | 1.1709 | 1.1531 | 1.1471 | 1.1339 | 1.12 | 1.109 | 1.1073 | 1.0666 | 1.0254 | 1.0065 | 1.0015 | 1
kbps

## Slide 28: Smart relay routing result
End-to-end round trip time
  In most countries, it has 5% ~ 30% reduction compared to traditional geo-aware DNS
Video bit rate
  In most countries, it has 5% ~ 70% increase compared to traditional geo-aware DNS

## Slide 29: Thank You
The presentation slides will be on our blog tomorrow: www.tango.me/blog
Questions: meng@tango.me
Visit our Tango Table for a Tango
T-shirt and speak to our recruiters!